## Slide 1: The Scrambling Process
The overall scrambling technique is to flip the frequency spectrum of a recorded audio clip around 3.5 kHz followed by the addition of a 8 kHz sine tone.
The actual flipped audio spectrum is produced by single-side band modulation of the original audio signal with a 7 kHz sine wave and by selecting the lower sideband signal. The Hibert Transform is used for single-sideband modulation in Matlab.

## Slide 2: Original and Scrambled Messages
The original and scrambled messages are plotted in the time- and frequency-domains below.
Both signals have the same tempo in the time-domain plot.
In the frequency-domain, you can see that the frequency spectrum of the original signal is flipped around 3.5 kHz with an extra tone at 8 kHz added.

## Slide 3: How to Descramble.
The overall steps for descrambling the message are
  Build a digital notch (bandstop) filter to remove the 8 kHz tone.
  Multiply the filtered signal with a 7 kHz tone which will then produce the original signal as well as an upper sideband signal.
  Build an external analogue low-pass filter to remove the unwanted upper sideband signal and keeping the desired lower sideband signal which is the original message. This analogue filter also serves as the anti-aliasing filter for the DAC.

## Slide 4: How to Descramble
A 8 kHz bandstop filter to remove the added tone
A lowpass filter (aprox. 5 kHz cutoff) to remove the upper sideband and keep the lower sideband signal which is our descrambled output. Also serves as the anti-aliasing filter after the DAC.
Scrambled audio input
Signal multiplication for spectrum flipping and hence descrambling
Descrambled audio output
A 7 kHz sine wave